STEPNC test – 7 inch Circle-Diamond-Square

Initial stock size – 12.0 x 12.0 x 2.90 aluminum with (4) bolt holes on 10.0 centers

Establish set point at center of stock – set ‘Z’ axis = .000 at 6” above stock locating surface

Info:	Program begins by facing entire stock to 2.820 thickness.

Program machines to within .100 of stock locating surface.

Completed 7 inch Circle-Diamond-Square

# Text boxes

X

Y

Stock Preparation:

Drill (4) 9/16 holes thru stock on 10 inch centers.

Counter-bore 1.00 dia x 1.0 depth

(or as req’d. to provide bolt head clearance when stock is faced to 2.80 thickness)

Cutting Tools Required:

- x .01 radius x 3.250 stickout 
(1.00 flute length minimum)

(Note:  Separate tools may be used for roughing & finishing, but are not required.)

Program machines down to within .100 of stock locating surface.

Entire stock is faced to 2.820 thickness at beginning of program.

X

Y