## Slide 1: Enabling the Advanced Manufacturing Environment
STEP Tools, Inc.
http://www.steptools.com
Martin Hardwick
Professor of Computer Science, RPI
President STEP Tools, Inc.
Team Leader, ISO STEP Manufacturing

## Slide 2: The advanced manufacturing problem
Solutions are machine and plant specific
  Machining programs are for one CNC and cannot be reused
  Drawings are hard to read and cannot be verified for completeness
  Solutions must be programmed in CAM, tested on the CNC and validated in CMM
  It takes a long time and the results are variable
1st draft CAM
2nd draft CAM
3rd draft CAM
Wait for operator to be ready
Enter model and most of drawing
Enter constraints not on drawing
Generate NC programs
1st draft CNC
2nd draft CNC
3rd draft CNC
Wait for CAM and CNC operators
Find the big errors
Wait for right tooling
Machine first part in wax
Wait for necessary fixtures
Machine first part in material
1st draft CMM
2nd draft CMM
3rd draft CMM
Wait for CAM and CMM operators
Check basic dimensions
Discover critical features
Measure critical features
Discover additional features
Verify part is correct
Enter rest of drawing
Create operations
Does it fit?
No time for robots and other automation

## Slide 3: Model Based Manufacturing solution
Models and processes are reused across enterprises
  Select best available machine
  Verify tooling and fixtures are compatible
  Optimize and/or edit using cloud services
  Measure continued conformance of final result
  Integrate robots using models
1st draft CAM
Select best available machine
1st draft CNC
1st draft CMM
Measure the model
Machine first part in material
It continues to fit!
Robots combine new paths with existing automation

## Slide 4: Enabling model based manufacturing
Business Process Modeling Notation
  Desired stages for the requested manufacturing task
  Inputs, outputs and operations described as process flow
  High level description, mostly graphical, but also formal
BPMN
STEP
Process solution for a manufacturing stage
  Product models for input and output, tooling and fixtures
  Operations defined in context to enable 3rd party optimization
  Machine independent but verifiable using CMM
MTConnect
Execution results for business analysis
  Detailed output steam of executed actions
  Feed back to update current state of stage model
  Feed forward for analysis by business systems
Design/Choose manufacturing solution
Design/Choose operation solution
Record results
Divide the manufacturing into stage models
  Each model has defined input and output requirements
  Each stage has a machine independent solution
  Each stage uses robot loaders and measurement devices

## Slide 5: Advanced Manufacturing Environment
Stage
Model
Model
Input
Stage
Model
Model
Results
Cloud Services
CMM
Adapter
MTConnect
Digital Infrastructure = UUID anchors, URL references, PPK signatures and fingerprints
“PMI for model based manufacturing”
Motions for precision
Tolerances for validation
To
Big data analysis
Model driven, coordinated motion with tolerance evaluation at key manufacturing stages
To BPMN
Process Flow
RBT
Adapter
Coordinates for placement
CNC
Adapter
Stage Model
Processor
From BPMN
Process Flow
Model
Question
Enhanced
Model
From
CAD/CAM and CAx

## Slide 6: Key points
Input is stage models
  Models previously developed for this task
PMI for intelligent machining
  The required geometry, dimensions and tolerances
Cloud services for optimization
  Rapid, inexpensive customization of previous solutions
Stage Model Processor
  Feeds codes, coordinates and PMI to the adaptors
  Prevents system collisions, monitors process conformance
Information Infrastructure
  UUID anchors to enable sharing with MTConnect and BPMN
  URL references to enable reuse across stages and assemblies
  Signatures to verify provenance and approval

## Slide 7: Development Tasks
Task 1 – Stage Model Processing
  Process selection and solution generation
  Real time simulation for coordination and validation
Task 2 – CNC Adaptor
  Volume removal and addition by precision machines
  Code generators with adaptive feedback
Task 3 – CMM Adaptor
  Model validation by measurement machines
  AP242 with PMI reader for ACIS
Task 4 – Robot Adaptor
  Product placement by learned path machines
  Coordinate generation and coordination
Task 5 – Digital Infrastructure
  GD&T data sharing across manufacturing assemblies and stages
  Integrity and authorization using signatures and fingerprints
Task 6 – MTConnect Modeling
  Schemas for communicating stage, process and machine models
  Protocols for coordination using execution results

## Slide 8: Demonstration scenario
Selected products and processes for demonstration?
  6 month proof of concept
  12 month feasibility testing
  18 month demonstration

## Slide 9: Summary
The AME will be:
  More automated because machines and robots will be coordinated
  More reliable because processes will be monitored and measured
  More flexible because processes will be machine independent
  More efficient because processes will be reused not redesigned
  More optimal because cloud services will customize
  More secure because data will be checked using signatures
  More scalable because models will be shared and reused