## Slide 1
STEP Tools, Inc.
http://www.steptools.com
Martin Hardwick
President STEP Tools, Inc.
Professor of Computer Science, RPI
Convener ISO STEP Digital Manufacturing
Standards for the Digital Thread
Integrated Measurement
February, 2017

## Slide 2: Smart Phone or Browser

## Slide 3: Scenario
Operation is close to its limits
  Tool wear issue
Remote operator wants it checked
  Probe plan determined in advance
  Initiated from a remote location
  Evaluated from a remote location

## Slide 4: Actions
Cutter sent from catalog with tool wear
Gcode sent to machine with probing macros and UUID’s for touch points
STEP sent to CMM with associations between touch points and tolerances
MTConnect sent from machine with probe results and UUID’s
QIF sent from CMM for evaluation

## Slide 5: Digital Thread
CNC Machine
Digital Twin Server
Smart
Metrology
Service
(Virtual CMM)
Smart
Tooling
Service
(Catalog)
G-code
AP242
Tooling
Inspection
Operation
QIF
Smart Phones and Tablets
MTConnect
AP242
HTML 5
2
3
4
5
1

## Slide 6: Evaluation
MTConnect
  Positional data, limits compliance
STEP
  CAD data, GD&T compliance
QIF
  Measurements, regulation compliance