## Slide 1: ISO 23247 Digital Twin Use case Testing
Scope reductions to enable August 25 completion
Results of June 23 Conference call

## Slide 2
OME
Core entity
User entity
User network
MES
ERP
Other
Twin
UI
Access network
Other
Data Sources
Resource access & interchange
sub-entity
Operation & management
sub-entity
Application & service
sub-entity
OME
DCDCE
(data collect only)
Adaptation, protocol translation
MTConnect agent, UMATI agent, ISA-88 state machine …
MTConnect client, UMATI client, ISA-88 client, …
Web Client
Web Server
Access network
Proximity network
EtherCAT, OPC-UA,
Profinet, Modbus, …
Service network
DCDCE: Data collection and device control entity
OME: Observable manufacturing element
(solid line): within scope of Digital Twin
(dotted line): out of scope of Digital Twin
Italic: Example protocol/implementation
Open API, administration shell
DCDCE
MTConnect agent, UMATI agent, ISA-88 state machine …
cloud
Super-visor
Access network
Legacy communication channel
PLM
ISO 23247-4 Figure A.1

## Slide 3
Use Case 1 – flexible schedule for robot drill & fill
On-shoring can increase by 50%

## Slide 4
User entity
Core entity
DCDCE
OME
Supervisory Control
Cell Controller
MOM
Coordinator
Combiner
PLM/ERP
Device Control
sub-entity
MTConnect
AP242
AP238
Rapid
(AP238 execution state)
State
Machine
(cell)
Robot1
State
Machine
(robot1)
Robot2,3,4
State
Machine
(robot2)
Data Collection
sub-entity
MTConnect Agent
Data
Cache
(cell)
AP238
State
Machine
(supervisory)
AP238
AP242
MTConnect
(ISA-88)
MTConnect
Translator
Models
Product/Process
Commands
Stop/Go, etc.
State Stream
Plunge complete, etc.
Instructions
Gcodes, etc.
Process Digital Twin
Wing Digital Twin
Data
cache
(process)
State
Machine
(process)
Data
cache
(wing)
State
Machine
(wing)
ISO 23247-4 Figure A.2
BOEING
Adjust schedule for
Completed ops
Unwanted ops
Unavailable robots

## Slide 5
Use Case 2 – weight reduction
Exact match of fastener to hole depth can reduce weight by 500lb

## Slide 6
User entity
Core entity
OME
Supervisory Control
Cell Controller
Measurement
Analyzer
Device Control
sub-entity
QIF Results
AP242
Caliper
State
Machine
(CMM)
Data Collection
sub-entity
Data
Cache
(caliper)
State
Machine
(supervisory)
QIF results
Planner
Models
Product/Process
Commands
Stop/Go, etc.
State Stream
Plunge complete, etc.
Measurements
Hole dimensions, etc.
Instructions
Gcodes, etc.
Part Digital Twin
AP242e2
Data
cache
MOM
PLM/ERP
AP242
ISO 23247-4 Figure A.4
LOCKHEED
Measure 3 ply’s
Compute stack up for each hole
Determine exact fastener length

## Slide 7
Use Case 3 – tool life optimization
Monitor tool
diameter
Compute tool
engagement
Store linked data
STEP-NC
MTConnect
Stream
results
Twin model
Machining
Context
Macros
Gcode
ops
STEP
Agent
Apply
Results
OMAC
ANSI
STEP Tools
ISO
Tool life can increase by 15%
Machine
parts

## Slide 8
User entity
Core entity
DCDCE
OME
Supervisory Control
Cell Controller
MOM
Tool Life Analyzer
PLM/ERP
Device Control
sub-entity
Process Digital Twin
Tool Digital Twin
MTConnect (with process and measurement)
Data
cache
(equipment)
AP242
ISO 13399
AP238
CNC
language
CNC
State
Machine
(CNC)
Data Collection
sub-entity
MTConnect Agent
Data
Cache
(controller)
AP238
AP238
AP242
AP239
Tweets (with process)
Translator
Data
cache
(process)
Models
Product/Process
Commands
Stop/Go, etc.
State Stream
Plunge complete, etc.
Measurements
Hole dimensions, etc.
Instructions
Gcodes, etc.
View3
Part Digital Twin
View2
View1
Data
cache
(part)
Combiner
AP242
ISO 23247-4 Figure A.3
SANDVIK
Caliper
State
Machine
(CMM)
Tweets (with measurement)
Measure actual tool wear
Estimate remaining life