## Slide 1: Digital Product Property Models
Ferroday Ltd
2023-01-20

## Slide 2: A material is a product and a product is a material

## Slide 3: Properties of products
A property of a product is a reaction of the product to its environment
The semantics of the property depend on the semantics of the environment
The property value depends on the values of the properties of the environment
Product testing to determine the value of a property has three possible functions:
  For quality assurance for procurement
  Trying to anticipate the environment of the service conditions
  Confirming that an engineering requirement has been achieved
All need to record the testing process and the environment
Notes: Those who just want to know only a property name and value are the equivalent of this who believe that the earth is flat

## Slide 4: ISO 10303-45 Materials and other engineering properties
Part of the Integrated Generic Resource of ISO 10303
  First published in 1995, the three schemas are now partly presented as modules
Defines a material property as a sub-type of a property of a product (Part 41) as a property that has dependencies
Specifies the representation of:
  the conditions on which the property value depends – the data environment
  the composition and structure of the product
  the value of a property including its representation as a mathematical expression
  the uncertainty of the value including a mathematical value
Illustrated by two instance diagrams for steel properties
Notes: The dependence of a property value on the data environment was represented in ISO 10303-45

## Slide 5: Measurement of a property value ISO 10303-235
Development originally established as a business need of Boeing.
The Chief Engineer wanted a traceable history for the origin and validation of a property value used in a design
  Particularly for when a part failed in service
I took over the development after Boeing pulled out after the AAM had been developed
This traceability can be illustrated in a diagram developed by consultation with Rodney Dreisbach (Boeing) and Keith Hunten (Lockheed Martin)

## Slide 6: Process model
Process
properties
Process
item
Process
record
Process
operation
Product
item
Resource
properties
Process
resource
Process
plan
Process
specification
uses
processed_by
recorded_by
produces
compliance_with
defines
Process
properties
has
has
specifies
used_by
Notes: All of the processes in the diagram ca be represented by the same model

## Slide 7: ISO 10303-235 Engineering properties and materials information (AP235)
The semantics of an engineering property is determined by the processes used in the test method
AP235 extends Part 45 to model the processes used to determine the property value
  Test data, certificated data, design data, design allowables
The process model implements ISO 10303-49 completely and so AP235 could be used for any process that results in a change in a property semantics and its value

## Slide 8: ISO 10303-235 Engineering properties and materials information – simplified view

## Slide 9: Scope of ISO 10303-235
Administrative
Dates, times, persons, organizations, addresses
Approvals, qualifications, certifications
Documents and files
Effectivity
External references
Languages
Locations
Requirements
Technical
Product and product history
Properties
Processes (Part 49)
Process resources and properties
Numerical and descriptive values
Mathematical expression values
Uncertainty and reliability of all values
Product substance composition and internal structure
Dimensions and tolerances

## Slide 10: Dictionary of test methods and properties
Notes: Kavka, V, Reference Dictionaries for Product Properties, Becker A.A, (ed) Metal Fabrication and Welding Technology, Nottingham 2003 (ISBN 0-85358-120-7)

## Slide 11: Conclusions
The technology for the representation of engineering product data developed by ISO/TC 184/SC4 has proved to be also valid for the representation of digital materials information since materials are products
The insights provided from materials knowledge were:
  the importance of the data environment to validate the property value
  The importance of the measurement method processes to provide the meaning of the value
The inclusion of the complete information model for a process could widen the application of AP235 to other processes in addition to testing and measurement