## Slide 1: UUIDs for Digital Twins
Saratoga Springs
Combined meeting of WG12 & WG15
“After the DMDII we travelled in different directions”
hardwick@steptools.com
Martin Hardwick
Convenor WG15

## Slide 2: Application twin modeling
Application interpreted model:
  Fundamental model of all products
  Normalized, integrated, unchanging
Application requirements model:
  Necessary model for a type of product
  Sufficient, unique, unambiguous
Application twin model:
  Fit for purpose model of a physical product
  Helpful, accurate, comprehensive

## Slide 3: EXAMPLE
IDENTIFIED ENTITY Drill_and_fill_twin SUBTYPE OF (Manufacturing_feature_twin); hole_in_place : BOOLEAN; -- in-place means is on the wing pilot_hole_in_place : BOOLEAN; tack_in_place : OPTIONAL AGGREGATION Product_view_twin; fastener_in_place : OPTIONAL AGGREGATION Product_view_twin; collar_in_place : OPTIONAL AGGREGATION Product_view_twin; washer_count : OPTIONAL count_measure; sealed : OPTIONAL AGGREGATION Product_view_twin; engineering_fit : OPTIONAL hole_class; disposition : drill_and_fill_condition; true_location : COMPOSITION geometric_tolerance_twin; true_size : COMPOSITION dimensional_size_twin; true_form : OPTIONAL COMPOSITION geometric_tolerance_twin; WHERE WR1: true_location.prototype ISA position_tolerance; WR2: true_size.prototype ISA diameter_size_tolerance; WR3: true_form.prototype ISA roundess_tolerance OR cylindricity_tolerance END_ENTITY;

## Slide 4: New keywords
The keyword IDENTIFIED is used for entities that have a (UUID) identity independent of the product model.
The keyword COMPOSITION is used to denote an existence dependency between two entities that have identity.
The keyword AGGREGATION is used to denote an accumulation of one identified entity within another identified entity.
The keyword OUTSIDE is used to indicate where information is useful outside of the file/context
Expect more

## Slide 5: Requirement
Clarity on the meaning of a UUID in SC4
  Does it identify a unique value or a unique existence
  Does it identify an AIM instance, ARM instance or ATM instance
  Does it belong to the enterprise or a CAD vendor
Or agree to disagree

## Slide 6: WG15 perspective
Every digital twin has a UUID
  Computed on demand
  Belongs to the enterprise
  After initial computation always the same
The digital twin can be composed and aggregated
  Build twins that are fit for purpose
  Out of other twins and ARM prototypes