## Slide 1: Part 21 Edition 3
DIS Testing Plan
Martin Hardwick
President STEP Tools, Inc.
Team Leader ISO STEP-Manufacturing
Professor of Computer Science, RPI

## Slide 2: P21 e3 Technical Summary
Anchor section enables references into the data
Reference section enables references out of the data
ZIP/directory organization for modularity and abstraction
Tags on anchors enable new kinds of data structures
Value names enable references to values
JavaScript binding enables intelligent applications
Signature section assures data source and prevents tampering
Character set updated to UTF-8 ISO 10646

## Slide 3: P21 e3 Functional Summary
Edition 3 adds references, intelligence and data structures to STEP, STEP-NC and IFC
  Massive shared product models
  Open and closed loop manufacturing
  Intelligent buildings
Sent to Geneva for DIS ballot
  Ongoing verification
  Open source examples on STEP Tools web site
  New projects starting

## Slide 4: Goals of Testing
Verify the draft standard
  Identify weaknesses
  Suggest corrections
Establish basic capability amongst tools kits
  Read/Write interoperability for anchors and references
  PMI and assembly test cases
  Digital signatures
Prepare for more rigorous testing after the DIS review
  Read/Write interoperability for CAx translators
  Support for end user test cases

## Slide 5: Scope
User oriented
  Assemblies
  PMI
  TDP
  Building management
Feature oriented
  Anchor
  Reference
  Zip
  Digital Signatures
PMI
Geometry
ISO-10303-21;
HEADER;
ENDSEC;
ANCHOR;
<as1_pe >= #10
ENDSEC;
REFERENCE;
#10 = <assembly.stp#root>;
#20 = <part/bolt.stp#bolt>;
#30 = <part/nut.stp#nut>;
#40 = <part/rod.stp#rod>;
#50 = <part/plate.stp#plate>;
#60 = <part/l-bracket.stp#l-bracket>;
ENDSEC;
END-ISO-10303-21;

## Slide 6: AP242 PMI Test Case
System U
  Writes geometry model
System A (ITI – 5/31)
  Reads geometry model
  Writes geometry model with anchors on selected faces
System B (STEP Tools – 6/30)
  Reads geometry model with anchors
  Writes PMI model that references the anchors
System C (All vendors)
  Read both models
  Merge and display to demonstrate PMI links
  CAX-IF meeting in September
PMI
Geometry

## Slide 7: AP242 Assemblies & ZIP
P21 e3 zip
  One STEP file for each component
  One STEP file for each sub-assembly
  One STEP file for complete assembly
Hand build a new ZIP for the AS1 assembly
  STEP Tools by 5/31
All vendors to read and display
  CAX-IF in September
ISO-10303-21;
HEADER;
ENDSEC;
ANCHOR;
<as1_pe >= #10
ENDSEC;
REFERENCE;
#10 = <assembly.stp#root>;
#20 = <part/bolt.stp#bolt>;
#30 = <part/nut.stp#nut>;
#40 = <part/rod.stp#rod>;
#50 = <part/plate.stp#plate>;
#60 = <part/l-bracket.stp#l-bracket>;
ENDSEC;
END-ISO-10303-21;

## Slide 8: Digital Signatures
STEP Tools writes signature on the PMI test case
ITI reads the signature, verifies source and checks for tampering
Repeat in other direction (ITI writes file, STEP Tools reads)
Schedule
  Verify basic capability 5/31
  Write PMI file with signature 6/30
  Read and verify signature 7/31
  Repeat in other direction 8/31
  Demonstrate at CAX-IF meeting in September

## Slide 9: Technical Data Package (wait for toolkit support)
AP203/214/242 file
Proprietary files
AP239 Manifest
Airbus Group to develop some scenario test data set
Share with group to determine how to support with P21 e3
Prepare a demonstration
New recommended practices

## Slide 10: IFC Building (wait for toolkit support)
System U
  Write a building
System A
  Splits out a room
  Write out building and room in two P21 e3 files
System B
  Read, change and write the room
System C
  Read building and show changed room